## Slide 1: Computer Architecture and Operating Systems CS 3230 :Assembly Section Lecture 4
Department of Computer Science and Software Engineering
University of Wisconsin-Platteville

## Slide 2: The MOV instruction
Move data
  From memory to a register
  From a register to memory
  From a register to another register
  Never from memory to memory
Syntax
  mov destination, source

## Slide 3: Addressing modes
Register
  MOV AX, BX
  MOV AL, BL
  MOV DX, SI
  MOV DS, BX
  Note: source/destination must be of identical size
Immediate
  Load a value to a register or a memory location
  MOV AX, 1234h

## Slide 4: Memory Addressing modes
Direct
  Move data from a memory location to a register
  Example :
    MOV AX, [1234h]
      1234h is an offset within the data segment DS
Register Indirect (base relative, or indexed)
  Offset is saved in a register
    BX, SI, DI define offset in the data segment
    BP defines an offset in the stack segment!
  Examples:
    MOV AX,[BX]
    MOV AX,[BP]
    MOV AX,[SI]
    MOV AX,[DI]

## Slide 5: Addressing modes
Base plus index (base relative indexed)
  Example:
    MOV AX, [BX+DI]
    MOV AX, [BX+SI]
    Base can be BX or BP, index SI or DI
Register relative
  Example:
    MOV AX, [BX+1234h]
    Register on the left can be BX, BP, SI, or DI
Base relative plus index
  Example:
    MOV AX, [BX+DI+1234h]
    Registers can be one of BX or BP and one of SI or DI

## Slide 6: Example: Memory and Labels
mov al, [L1] ;copy byte at L1 into al
mov eax, L1 ;eax = address of byte at L1
mov [L1], ah ;copy ah into byte at L1
mov eax, [L6] ;copy double word at L6 into eax
add eax, [L6] ;eax += double word at L6
add [L6], eax ;double word at L6 += eax
mov al, [L6] ;copy first byte of double word at L6
;into al
mov [L6],1 ;generates “operation size not ;specified” error
mov dword[L6],1 ;stores 1 in double word at L6

## Slide 7: Debugging
There are four debugging routines named:
  dump_regs: this macro prints out the values of the registers (in hexadecimal)
    Syntax : dump_regs X
    X: It takes a single integer argument that is printed out as well. This can be used to distinguish the output of different dump regs commands
  dump_mem: this macro prints out the values of a region of memory (in hexadecimal) and also as ASCII characters
    Syntax: dump_mem X, label , Y
    X: This can be used to distinguish the output of different dump_mem commands
    Label: the starting address of displayed region
    Y: the number of 16-byte paragraphs to display after the starting address
    Note: The memory displayed will start on the first paragraph boundary before the requested address

## Slide 8: Debugging (cont.)
There are four debugging routines named:
  dump_stack: this macro prints out the values on the CPU stack
    Syntax: dump_stack X, Y , Z
    X: This can be used to distinguish the output of different dump_stack commands
    Y: the number of double words to display below the address that the EBP register holds
    Z: the number of double words to display above the address in EBP
  dump_math: this macro prints out the values of the registers of the math coprocessor
    Syntax: dump_math X
    X: This can be used to distinguish the output of different dump_math commands

## Slide 9: Important Flags
Z – set when the result of the last operation was zero
C – Set when there was a carry (or borrow) beyond the most significant bit in the last operation (unsigned overflow)
O – Set when the last operation overflowed, when interpreting the operands as signed
P – Indicates the parity of the result of the last operation (is set when the destination has an even number of 1 bits)
S – The sign bit (MSB) of the result of the last operation
D – direction flag, controls the direction of a string stored in memory (more later)
Notes: Carry flag same as operation flag – carry with unsigned and operation with signed
Ex: show the flags after: 101101 + 1101100
= 1001001
doesn’t equal zero, so Z = 0
last bit was carried, so C = OF = 1
odd number of 1’s, so P = 0
MSB is 1 (negative), so S = 1

## Slide 10: Addition
ADD X,Y
  X=X+Y
  X, Y can be register or memory, but not both memory
  Y can also be immediate data
Some modified flags: S, C, Z, O,P
Examples
  ADD AX, BX ; register addition
  ADD AX, 5h ; immediate addition
  ADD [BX], AX ; addition to memory location
  ADD AX, [BX] ; memory location added to register
  ADD DI, MYVAR ; memory offset added to the register

## Slide 11: Increment
INC X
  X can be register or memory location
  X=X+1
Some modified flags: S, Z, O, P
Examples:
  INC AX ; AX=AX+1
  INC byte [BX] ; memory location increased by 1
  INC word [BX] ; memory location increased by 1
Notes: Remember: memory location needs to specify size

## Slide 12: Subtraction
SUB X,Y
  X=X-Y
  X, Y can be register or memory, but not both memory
  Y can also be immediate data
Sub is performed using 2’s (see the handout)
Some modified flags: S, C, Z, O,P
Examples
  SUB AX, BX ; register addition
  SUB AX, 5h ; immediate addition
  SUB [BX], AX ; addition to memory location
  SUB AX, [BX] ; memory location added to register
  SUB DI, MYVAR ; memory offset added to the register

## Slide 13: Decrement
DEC X
  X can be register or memory
  X=X-1
Some modified flags: S, Z, P, O
Examples
  DEC AX ; AX=AX-1
  DEC BYTE [BX] ; memory location decreased by 1
  DEC WORD [BX] ; memory location decreased by 1
Notes: NEG instruction: negative of the number
Example:
mov eax, 4
neg eax  eax = -4
Memory needs size

## Slide 14: 64 Bits Addition in X86
Add with Carry Instruction
ADC X,Y
  X= X + Y + Carry flag
  X, Y can be register or memory, but not both memory
  Y can also be immediate
Example: (EBX:EAX) + (EDX:ECX)
  ADD EAX,ECX
  ADC EBX,EDX
Some modified flags: S, C,Z, O, P
Notes: How to save 64-bit number in Register: save the lower 32 bits in RX, save upper 32 bits in RY (saved in two different registers)
Represent the number: (Upper location: loxer location), so above example would be (RY:RX)
Hexa example: 3CA986B53B2A0112 = EBX:EAX
EBX EAX
To add 2 64-bit numbers, lower part is just simple ADD instruction, but upper part needs to be ADC to include the carry from the lower part.

## Slide 15: 64 Bits Subtraction in X86
Sub with Borrow Instruction
SBB X,Y
  X=X - Y - Carry flag
  X, Y can be register or memory (not both memory)
  X can be immediate
Some modified flags: S, C, Z, P, O
Example: (EBX:EAX) – (ESI:EDI)
  SUB EAX, EDI
  SBB EBX, ESI
Notes: Same with ADC

## Slide 16: MUL Instruction
The MUL (unsigned multiply) instruction multiplies an 8, 16, or 32-bit operand by either AL, AX, or EAX
The instruction formats are:
  MUL Reg/Mem8
  MUL Reg/Mem16
  MUL Reg/Mem32
Results are saved as following
Notes: Example: move al, -1
What is the value of each if we consider the value as signed and as unsigned?
AL: 11111111
if signed: -1
if unsigned: 255
Since the number is different, we need different multiply instructions
1) MUL: consider the contents of the registers as unsigned numbers
2) syntax: MUL X (single operand)
8 bits: if AH = 0  CF = OF = 0
else CF = OF = 1
16 bits: if DX = 0  CF = OF = 0
else CF = OF = 1

## Slide 17: MUL Examples
17
100h * 2000h, using 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
The Carry flag indicates whether or not the upper half of the product contains significant digits.
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 18: Signed Integer Multiply
18
IMUL (signed integer multiply ) multiplies an 8, 16, or 32-bit signed operand
The instruction formats are:
  Imul source1
  imul dest, source1
  imul dest, source1, source2
    Note: source2 should be an immediate value
Notes: Syntax similar to mul instruction

## Slide 19: IMUL Instruction
19
Notes: If AH = sign extension of AL (all 0’s: +; all 1’s: -)  CF = OF= 0
If DX = sign extension of AX (all 0’s: +; all 1’s: -)  CF = OF= 0
If EDX = sign extension of EAX (all 0’s: +; all 1’s: -)  CF = OF= 0
Example:
Mov al, 10
Mov bl, -1
IMUL bl
AX = -10 = 11110110 (remember -128 ≤ AL ≤ 127 in signed number)
So AH will be all 1’s (the sign of -10) since -10 fits in AL, hence CF = OF = 0

## Slide 20: DIV Instruction
20
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV Reg/Mem8
    DIV Reg/Mem16
    DIV Reg/Mem32
Notes: When dividing, you have to initialize edx to avoid error
mov edx, 0
Same syntax as mul and imul

## Slide 21: DIV Examples
21
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 3
Same division, using 32-bit operands:
mov edx,0 ; clear dividend, high
mov eax,8003h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = 00000080h, EDX = 3

## Slide 22: Unsigned Size Increase
How about increasing the size of a 2-byte quantity to 4 byte?
Therefore, there is an instruction called movzx (Zero eXtend), which takes two operands
  Destination: 16- or 32-bit register
  Source: 8- or 16-bit register, or 1 byte in memory, or 1 word in memory
  The destination must be larger than the source!
Notes: 22

## Slide 23: Using MOVZX
movzx eax, ax ; extends ax into eax
movzx eax, al ; extends al into eax
movzx ax, al ; extends al into eax
movzx ebx, ax ; extends ax into ebx
movzx ebx, [L] ; gives a “size not specified” error
movzx ebx, byte [L] ; extends 1-byte value at address L into ebx
movzx eax, word [L] ; extends 2-byte value at address L into eax
Notes: 23

## Slide 24: Signed Size Increase
There is no way to use movzx instructions to increase the size of signed numbers, because of the needed sign extension
New conversion instructions with implicit operands
  CBW (Convert Byte to Word): Sign extends AL into AX
  CWD (Convert Word to Double): Sign extends AX into DX:AX
  CWDE (Convert Word to Double word Extended): Sign extends AX into EAX
  CDQ (Convert Double word to Quad word): Signs extends EAX into EDX:EAX (implicit operands)
Notes: 24
Add CDQ in program 1