## Slide 1: Computer Architecture and Operating Systems CS 3230 :Assembly Section Lecture 6
Department of Computer Science and Software Engineering
University of Wisconsin-Platteville

## Slide 2: Logic instructions
NOT, AND, OR, XOR
  NOT X ; X = ~X
  AND X, Y ; X = X & Y
  OR X, Y ; X = X | Y
  XOR X, Y ; X = X ^ Y
NOT does not modify any flag
The other instructions affect
  C , O, Z, S, P
Notes: Example:
AL = 1001111
BL = 01100100
And AL, BL  AL = AL & BL
AL = 00000100
X Y OR AND XOR
0 0 0 0 0
0 1 1 0 1
1 0 1 0 1
1 1 1 1 0

## Slide 3: Bit masking and flipping
Suppose AL = 00101100b
Masking: if you only need the lower four bits (i.e. 1100)
  mov al, 00101100b
  mov ah, 00001111b
  and al, ah ; --> now al = 00001100b
Flipping: to flip the middle four bits of AL
  mov al, 00101100b
  mov ah, 00111100b
  xor al, ah ; --> now al = 00010000b
Notes: Bit masking: AL = 11001110
- keeps the lower 4 bits
Result: 00001110
Masking: keep 2, 3, 4, 7
AL = 11001110
Desired Result: 10001100
so,
Mov ah, 10011100
And al, ah
- Now AL = 10001100

## Slide 4: The TEST instruction
TEST is a non-destructive version of AND
  Logically ANDs two operands as AND would
  Modifies FLAG bits like AND
  Does not modify the contents of the destination
  TEST AL,1 sets flags like AND AL,1 but does not modify AL
  Useful prior to jump instructions

## Slide 5: Shift Left
Syntax SHL reg, count
  Count could be immediate or in register value
Result:
  Moves the left operand a bit position to the left as many times as specified by count or CL
  The empty positions are filled with 0’s
  The higher order (H.O) bit is stored in the C flag
  The most efficient way to multiply by 2
0
Register
C
SHL

## Slide 6: Shift Left: Application
Here is a code snippet that counts the number of bits that are “on” (i.e. 1) in the EAX register

## Slide 7: Shift Right
Syntax SHR reg, count
  Count could be immediate or in register value
Result:
  Moves the left operand a bit position to the right as many times as specified by count or CL
  The empty positions are filled with 0’s
  The lower order (L.O) bit is stored in the C flag
  The most efficient way to divide by 2
Register
C
SHR
0
Notes: Example:
AL = 11001001
SHR AL, 1
AL = 01100100

## Slide 8: Shift Arithmetic Right
Syntax SAR reg, count
  Count could be immediate or in register value
Result:
  Moves each bit of the operant one position to the right as many times as specified by count/CL
  Lower order bit shifts to the carry flag
  High order bit is replicated
Register
C
SAR
Notes: Example:
AL = 11001001
SAR AL, 1
AL = 11100100
Keeps most significant bit the same

## Slide 9: Shift Arithmetic Left
This instruction is just a synonym for SHL
  It is assembled into the exactly the same machine code as SHL

## Slide 10: Rotate Through Carry L/R
Left: Syntax RCL reg, count
  Count could be immediate or in register value
  Rotate bits to the left through the carry flag
  Bit in the carry flag is written back to bit 0
Right: Syntax RCR reg, count
  Count could be immediate or in register value
  Rotate bits to the right through the carry flag
  Bit in the carry flag is written back to H.O. bit
RCL
RCR

## Slide 11: Rotate Left/Right
Left: Syntax ROL reg, count
  Count could be immediate or in register value
  Rotate bits to the left
  H.O. bit goes to the L.O. bit and the carry flag
Right: Syntax ROR reg, count
  Count could be immediate or in register value
  Rotate bits to the right
  L.O. bit goes to the H.O. bit and the carry flag
ROL
ROR
Notes: Old carry is discarded

## Slide 12: Examples
mov ax,3 ; Initial register values AX = 0000 0000 0000 0011
mov bx,5 ; BX = 0000 0000 0000 0101
or ax,9 ; ax <- ax | 0000 1001 AX = 0000 0000 0000 1011
and ax,10101010b ; ax <- ax & 1010 1010 AX = 0000 0000 0000 1010
xor ax,0FFh ; ax <- ax ^ 1111 1111 AX = 0000 0000 1111 0101
Neg ax ; ax <- (-ax) AX = 1111 1111 0000 1011
Not ax ; ax <- (~ax) AX = 0000 0000 1111 0100
or ax,1 ; ax <- ax | 0000 0001 AX = 0000 0000 1111 0101
shl ax,1 ; logical shift left by 1 bit AX = 0000 0001 1110 1010
shr ax,1 ; logical shift right by 1 bit AX = 0000 0000 1111 0101
ror ax,1 ; rotate right (LSB=MSB) AX = 1000 0000 0111 1010
rol ax,1 ; rotate left (MSB=LSB) AX = 0000 0000 1111 0101
mov cl,3 ; Use CL to shift 3 bits CL = 0000 0011
shr ax,cl ; Divide AX by 8 AX = 0000 0000 0001 1110
mov cl,3 ; Use CL to shift 3 bits CL = 0000 0011
shl bx,cl ; Multiply BX by 8 BX = 0000 0000 0010 1000